BT1	Battery holder, 2x AA	BC2AAPC-ND
Included separately

C1, C2, C4	Cap, Tantalum, 4.7µF [0805]	478-8125-1-ND
Polarized (match PCB mark to part mark)

C3, C5, C6	Cap, Ceramic, 1.5nF [0805]	1276-1794-1-ND

C7, C8, C11, C12, C13	Cap, Ceramic, 2.2µF [0805]	587-1293-1-ND

C9, C10	Cap, Ceramic, 22µF, [1206]	399-8183-1-ND

D1, D2	Diode, Schottky, 1A	SS12-E3/61TGICT-ND
Polarized (match PCB mark to part mark)

D3	Diode, dual Schottky	BAT54SFSCT-ND

DS1, DS2, DS3	LED, red	SML-D12U1WT86CT-ND
Polarized (match diode symbol on PCB to symbol on back of part)

J3	3.5mm mono phone jack	CP-3523MJCT-ND
Connector for headphones

J4	2.5mm mono phone jack	CP-2523MJCT-ND
Connector for magnetic loop probe

J4(p)	2.5mm mono phone plug	CP3-1004-ND
Connector for magnetic loop probe - see probe construction guide

L1	100uH inductor	RLB0914-101KL-ND

Q1, Q3	P-channel MOSFET, 3.7A	IRLML6402PBFCT-ND

Q2	Low threshold N-channel MOSFET	FDV301NCT-ND

R1, R10, R11, R15	Res, 15 ohm 5% [0805]	RMCF0805JT15R0CT-ND

R2, R8	Res, 100 ohm, 1%, [0805]	311-100CRCT-ND

R3, R6, R7, R9, R12, R16	Res, 10k ohm, 1%, [0805]	311-10.0KCRCT-ND

R4	Res, 1 ohm 5% [1206]	1276-5843-1-ND

R5, R13	Res, 1k ohm, 1% [0805]	311-1.00KCRCT-ND

R14: DO NOT POPULATE

RV1	Pot, 100k ohm	3352T-104LF-ND
Leads bent for packing; bend back gently

SW1, SW2	Switch, tactile	450-1140-ND

U1	Microcontroller, XMEGA (AVR)	ATXMEGA32E5-AU-ND
Flashed with bootloader https://github.com/alexforencich/xboot

U2	Dual op-amp, low noise OPA1662	296-36692-1-ND

U3	Dual logic inverter, 74HC04	1727-6914-1-ND